# Calculating Integrals and Statistics on Intervals using Fit Plot
Setting of intervals in Fit interval tab of Fit Plot was initially intended for specifying the range of data which are used for fitting by sum of fit curves. However, this tab can also be used to calculate integrals and statistics on these intervals. Data-Baseline is used to calculate the results.
## Peak Moments
MagicPlot can integrate data on selected intervals and calculate peak moments (x mean, variance, skewness, kurtosis). Spectrum line is treated as probability distribution curve: x values are treated as 'independent variable' and y values are treated as 'probability'. Standard statistical formulas are used to calculate moments (see below).
Statistical data and integrals are automatically updated if x or y data are changed or intervals are changed.

Integration on intervals
All statistical data are summarized in the intervals table:

Statistics on intervals
## Managing Intervals
Move interval borders with mouse. Double click on interval to split it at desired position. Right click opens context menu from which new intervals can be created on free space and existing intervals can be deleted or split.
## Relative Integrals Calculation
MagicPlot can calculate relative integrals to compare the relative intensity of spectrum lines. To compute relative integrals set Relative integrals checkbox. MagicPlot designate the smallest integral as 1, but you can enter a custom value. If you want to set not the smallest integral as a reference point, enter 1 first and then enter the value of desired integral relative to 1 into this field, so that other integrals will be calculated relative to this new value.
## Computational Formulas
Central moments are calculated as follows (see table). All sums are calculated using compensated summation. Central moments are calculated on second pass after Mean calculation.
Property	Formula
n	The number of non-NaN (x,y) points
Y Sum (normalization)
X Mean (first moment)
2, 3, 4th Central moments

MagicPlot uses the following formulas to calculate intervals statistics:
Property	Formula
Integral	Calculated using Trapezoidal rule
X Mean (expected value)
Variance
Standard deviation
Skewness
Kurtosis

## See Also
- Nonlinear Curve Fitting: Fit Plot
- Using Spline for Baseline Subtraction
- Descriptive Statistics